## Slide 1: Efficient Latency Guarantees for Mixed-criticality Networks-on-Chip
CPSWeek • RTAS 2017
18. April 2017, Pittsburgh, PA, USA
Sebastian Tobuschat, Rolf Ernst
IDA, TU Braunschweig, Germany

## Slide 2: Current and Future Embedded Systems
multicore architectures are reaching safety-critical embedded systems
  e.g. sensor fusion and recognition in highly automated driving
integrate previously distributed functions in a single chip
     mixed-criticality systems
standards require isolation in case of shared resources
  e.g. IEC 61508: “sufficient independence”

## Slide 3: Networks-on-Chip (NoC)
offer high-performance, scalability and flexibility
transmissions share NoC resources
  e.g. buffers, links
 provide isolation
consequences
  highest relevant safety level for shared parts
     expensive
  or implement “sufficient independence”
   Quality of Service mechanisms (QoS)
  main Challenge: QoS guarantees + high performance

## Slide 4: Providing Quality of Service – Related Work
static partitioning (e.g. TDMA):
  e.g. [Milberg2004], [Goossens2010], [Psarras2015], [Panades2006], [Hansson2007]
   typically reduced utilization
prioritization:
  e.g. [Bolotin2004], [Bjerregaard2005]
  “criticality as priority”
   reduced performance for BE
dual Priority:
  e.g. [Burns2014], [Indrusiak2015]
  based on behavior of safety-critical sender:
    send with either high or low priority
  not accounting for NoC load; only for whole path
   reduced exploitation of latency slack

## Slide 5: Providing Quality of Service – Related Work
static partitioning (e.g. TDMA):
  e.g. [Milberg2004], [Goossens2010], [Psarras2015], [Panades2006], [Hansson2007]
   typically reduced utilization
prioritization:
  e.g. [Bolotin2004], [Bjerregaard2005]
  “criticality as priority”
   reduced performance for BE
dual Priority:
  e.g. [Burns2014], [Indrusiak2015]
  based on behavior of safety-critical sender:
    send with either high or low priority
  not accounting for NoC load; only for whole path
   reduced exploitation of latency slack
Goal: minimize negative performance impact of QoS mechanisms (on non-critical senders)
Idea: prioritize BE to exploit (latency) slack of critical applications

## Slide 6: Outline
Motivation
Providing Quality of Service
Latency Guarantees
Experimental Results
Conclusion
Notes: 2

## Slide 7: Idea
latency slack
  difference between worst-case latency and deadline
safety critical applications do not benefit from finishing before deadline
but BE applications benefit from low latency
baseline approach:
  two traffic classes: guaranteed latency (GL) and best effort (BE)
  prioritize BE over GL and limit interference BE induces to GL to exploit slack of GL
utility function of a firm/hard real-time task (Stankovic1998)
utility(f)
finishing time f
deadline

## Slide 8: Limit BE Interference
extend (GL) packet header with blocking counter (BC)
  packet or flit level (tradeoff: performance and overhead)
    for small or single size packets  packet level sufficient
    different sizes or more fine granular  flit level
BC is evaluated and adapted in each router
  decremented when packet is blocked by higher priority packet (this can be BE or other GL with BC=0)
if BC of a packet/flit reaches zero:
  prioritize queue containing it over BE, until no packet/flit with BC=0 is remaining
    other implementation possible: sorting, forwarding/overtaking

## Slide 9: Blocking Counter
header field allows to freely distributed the allowed blocking on the path, based on actual needs of BE
  account for local or temporary traffic hot spots
initial value obtained from analysis
  optimization problem: find initial BC value that minimizes slack, while all (GL) streams are schedulable
can account for local behavior of sender and (online) adapt BC on packet level
  e.g. using sender information (cf. [Burns2014], [Indrusiak2015])
  e.g. allow mode change, software update, task re-mapping

## Slide 10: Outline
Motivation
Providing Quality of Service
Latency Guarantees
Experimental Results
Conclusion
Notes: 2

## Slide 11: Worst-case Latency
based on [Rambo2015] – compositional performance analysis
local router analysis
  worst-case multiple activation processing time for a stream
    maximum time resource (router) is busy processing q flits of a stream
    used to derive worst-case latency of each hop
  break down into sum of different terms addressing different blocking factors
for each stream
    analyze routers along its path and propagate event models downstream
formally analyze routers iteratively

## Slide 12: Worst-case Multiple Activation Processing Time
Arbitration
Output 1
Input 1
2
2
BE
GL
State norm
Input n
1
1
BE
GL
Output n
…
…
For details and equations look into the paper
: number of flits
: arrival time of event q
C : single flit transmission time

## Slide 13: Worst-case Multiple Activation Processing Time
Arbitration
Output 1
Input 1
2
2
BE
GL
State norm
Input n
1
1
BE
GL
Output n
…
…
For details and equations look into the paper
: number of flits
: arrival time of event q
C : single flit transmission time
flit transmission

## Slide 14: Worst-case Multiple Activation Processing Time
Arbitration
Output 1
Input 1
2
2
BE
GL
State norm
Input n
1
1
BE
GL
Output n
…
…
For details and equations look into the paper
: number of flits
: arrival time of event q
C : single flit transmission time
interference at output

## Slide 15: Worst-case Multiple Activation Processing Time
Arbitration
Output 1
Input 1
1
1
2
2
BE
GL
State norm
Input n
1
1
BE
GL
Output n
…
…
For details and equations look into the paper
: number of flits
: arrival time of event q
C : single flit transmission time
interference at input

## Slide 16: Worst-case Multiple Activation Processing Time
Arbitration
Output 1
Input 1
1
1
2
2
BE
GL
State norm
Input n
1
1
BE
GL
Output n
…
…
For details and equations look into the paper
: number of flits
: arrival time of event q
C : single flit transmission time
new interference through BC
t=0

## Slide 17: Worst-case Multiple Activation Processing Time
Arbitration
Output 1
Input 1
1
1
1
1
BE
GL
State norm
Input n
1
1
BE
GL
Output n
…
…
For details and equations look into the paper
: number of flits
: arrival time of event q
C : single flit transmission time
new interference through BC
t=1
send BE
and
decrement BC

## Slide 18: Worst-case Multiple Activation Processing Time
Arbitration
Output 1
Input 1
1
1
0
0
BE
GL
State norm
Input n
1
1
BE
GL
Output n
…
…
For details and equations look into the paper
: number of flits
: arrival time of event q
C : single flit transmission time
new interference through BC
t=2
send BE
and
decrement BC

## Slide 19: Worst-case Multiple Activation Processing Time
Arbitration
Output 1
Input 1
1
1
0
0
BE
GL
State crit
Input n
1
1
BE
GL
Output n
…
…
For details and equations look into the paper
: number of flits
: arrival time of event q
C : single flit transmission time
new interference through BC
t=3
as BC=0
send GL

## Slide 20: Interference through BC
additional blocking allowed by the blocking counter (BC)
depends on:
  higher priority traffic (BE or GL with BC=0)
  blocking counter
part of event model propagation
: packet sitze in flits
C : single flit transmission time
  : maximum number of flits that arrive in
  : set of streams with higher priority than i
current value of BC (in flits)
number of interfering flits
For details look into the paper

## Slide 21: Outline
Motivation
Providing Quality of Service
Latency Guarantees
Experimental Results
Conclusion
Notes: 2

## Slide 22: Evaluation
OMNeT++ framework + HNOCs library
one VC for GL; 4 VCs for BE
buffer size: 6 packets
router with 4 stage pipeline
packet size: 4 flits
XY-routing
BC counting flits
two sets of experiments:
  synthetic workload: general properties
  benchmark based: performance improvement

## Slide 23: Experiment 1
synthetic workload, simple line topology
  periodically injecting packets
  injection jitter: 25% of period
  increase load  decrease period
  one GL stream overlapped by four BE streams
  different values for BC (note BC=0  classic prioritization)
R
CPU
R
CPU
R
CPU
R
CPU
R
CPU
R
CPU
R
CPU
τ1
τ2
τ3
τ4
τ5
τ7
τ6
GL communication
BE communication

## Slide 24: Experiment 1 – GL Latency (τ1)
GL load: 0.1 flits/cycle/node (i.e. 10% link bandwidth)
analyzed latency increases with BC

## Slide 25: Experiment 1 – BE Latency
BE load: 0.2 flits/cycle/node (i.e. 20% link bandwidth)
latency of τ2 (solid) and τ5 (dashed)
performance gain is higher for BE senders close to GL and for higher BC values

## Slide 26: Experiment 1 – GL Backlog (τ1)
BE load: 0.2 flits/cycle/node (i.e. 20% link bandwidth)
possible backlog increases with BC and load

## Slide 27: Experiment 2
benchmark based
  traces from CHStone
    extracted using Gem5: ARMv7, 32kB L1
    accesses to network (e.g. memory access, communication, cache access)
  random destinations
  random mappings of interfering load
  latency for highlighted BE node

## Slide 28: Experiment 2 – Random Destinations - BE Latency
45% lower average latency
increased jitter (for BE)
latency normalized to average latency of HP
distribution over all mappings

## Slide 29: Synthesis Results
2x2 NoC, 5 VCs, buffer size of 6 packets per VC
Virtex-6 LX760 FPGA, Xilinx ISE 14.6, standard settings
4 approaches
  baseline: round robin
  FP: one prioritized VC for GL (RR for requests of the same priority)
  DP: flag to change priority of GL (i.e. higher or lower than BE)
  BC: proposed approach (priority change on BC value)
Unit | Baseline | FP | DP | BC
#Registers | 9365 | 9395 | 9389 | 9740
#LUTs | 12149 | 12205 | 12199 | 12688
Freq. (MHz) | 210 | 210 | 210 | 210
+4.5%
+4.0%

## Slide 30: Outline
Motivation
Providing Quality of Service
Latency Guarantees
Experimental Results
Conclusion
Notes: 2

## Slide 31: Conclusion
run-time configurable, dynamic prioritization of GL to exploit latency slack of safety-critical applications
  based on actual blocking through BE
  prioritize BE over GL when possible
increased performance for BE
  up to 45% lower average latency
increased jitter
less than 5% hardware overhead (for non optimized solution)
future work:
  evaluate different strategies for BC (e.g. limit end-to-end and per router)
  account for backpressure
Thank you for your attention.
Questions?

## Slide 32: References
[Bjerregaard2005]T. Bjerregaard and J. Sparsoe, “Scheduling discipline for latency and bandwidth guarantees in asynchronous network-on-chip,” in Asynchronous Circuits and Systems, 2005. ASYNC 2005. Proceedings. 11th IEEE International Symposium on, pp. 34–43, March 2005.
[Bolotin2004] E. Bolotin, I. Cidon, R. Ginosar, and A. Kolodny, “QNoC: QoS architecture and design process for network on chip,” J. Syst. Archit., vol. 50, pp. 105–128, Feb. 2004.
[Burns2014] A. Burns, J. Harbin, and L. Indrusiak, “A wormhole NoC protocol for mixed criticality systems,” in Real-Time Systems Symposium (RTSS), 2014 IEEE, pp. 184–195, Dec. 2014.
[Goossens2010] K. Goossens and A. Hansson, “The aethereal network on chip after ten years: Goals, evolution, lessons, and future,” in Proceedings of the 47th Design Automation Conference, DAC ’10, (New York, NY, USA), pp. 306–311, ACM, 2010.
[Hansson2007] A. Hansson, M. Coenen, and K. Goossens, “Channel trees: Reducing latency by sharing time slots in time-multiplexed networks on chip,” in CODES+ISSS, pp. 149–154, Sept 2007.
[Indrusiak2015] L. Indrusiak, J. Harbin, and A. Burns, “Average and worst-case latency improvements in mixed-criticality wormhole networks-on-chip,” in Real-Time Systems (ECRTS), 2015 27th Euromicro Conference on, pp. 47–56, July 2015.
[Milberg2004] M. Millberg, E. Nilsson, R. Thid, and A. Jantsch, “Guaranteed bandwidth using looped containers in temporally disjoint networks within the nostrum network on chip,” in Design, Automation and Test in Europe Conference and Exhibition, 2004. Proceedings, vol. 2, pp. 890–895 Vol.2, Feb 2004.
[Panades2006] I. Miro Panades, A. Greiner, and A. Sheibanyrad, “A low cost network-on-chip with guaranteed service well suited to the gals approach,” in Nano-Networks and Workshops, 2006. NanoNet ’06. 1st International Conference on, pp. 1–5, Sept 2006.
[Psarras2015] A. Psarras, I. Seitanidis, C. Nicopoulos, and G. Dimitrakopoulos, “Phasenoc: Tdm scheduling at the virtual-channel level for efficient network traffic isolation,” in Proceedings of the 2015 Design, Automation & Test in Europe Conference & Exhibition, DATE ’15, (San Jose, CA, USA), pp. 1090–1095, EDA Consortium, 2015.
[Rambo2015] E. A. Rambo and R. Ernst, “Worst-case communication time analysis of networks-on-chip with shared virtual channels,” in Proceedings of the 2015 Design, Automation & Test in Europe Conference & Exhibition, DATE ’15, (San Jose, CA, USA), pp. 537–542, EDA Consortium, 2015.

## Slide 33: Back Up
Backup Slides

## Slide 34: Experiment 2 – Hot Module - BE Latency
all nodes sending to memory
distribution over all mappings

## Slide 35: Operational Example (step 0)
Arbitration
Input
1
1
BE
GL
Output 1
State norm
t=0
Router in normal state (i.e. BE has high priority)
Two GL packets (with BC=1) waiting

## Slide 36: Operational Example (step 1)
Arbitration
Input
2
1
BE
GL
Output 1
State norm
t=1
1
GL packet is sent
BE packet arrives

## Slide 37: Operational Example (step 2)
Arbitration
Input
2
0
BE
GL
Output 1
State norm
t=2
Send BE packet, as GL still allows blocking
  BC of GL is decremented
New BE packet arrives

## Slide 38: Operational Example (step 3)
Arbitration
Input
2
BE
GL
Output 1
State crit
t=3
0
GL achieves higher priority (as BC==0)
  Send GL packet, BE is blocked
New BE packet arrives

## Slide 39: Operational Example (step 4)
Arbitration
Input
2
2
BE
GL
Output 1
State norm
t=4
Send BE packet (as no GL was waiting)
New GL packet arrives

## Slide 40: Operational Example (step 5)
Arbitration
Input
2
1
BE
GL
Output 1
State norm
t=5
Send BE packet, as GL still allows blocking
  BC of GL is decremented
   BE achieves lower latency

## Slide 41: Operational Example (step 6)
Arbitration
Input
2
1
BE
GL
Output 1
State norm
t=6
1
Send GL packet (with BC>0) as no BE is waiting

## Slide 42: Compositional Performance Analysis for NoCs
based on analysis from [Rambo2015]
analysis performed iteratively
step 1: local analysis (at each router)
  compute worst-case latency of flits based on critical instant (busy window)
  derive output event models
step 2: global analysis
  propagate event models downstream
  go to step 1 if any event model has changed
  otherwise, terminate
Input Event Models
Local
Scheduling Analysis
Output Event Models
Convergence or
Non-Schedulability ?
No
Environment Model
Terminate

## Slide 43: CPA Approach
worst-case end-to-end latency relies on response times from local analyses
for each stream
    analyze routers along its path and propagate event models downstream
formally analyze routers iteratively
Router 1
Router 2
Sink 2
Sink 1
Source

## Slide 44: Mapping NoC Domain to Processor Resource Model
output ports  processing resources
input ports  shared resources with mutually exclusive access
traffic stream  chain of tasks mapped to resources
flit transmission  task execution
flit arrival  task activation
  input and output event models

## Slide 45: Network Latency
derive single hop latency based on
  multiple activation busy time
  router’s overhead (e.g. time to determine and acquire output port)
network latency :
  sum of single hop latencies on path
  + injection time (including backpressure at source)
  + de-/packetization overhead

## Slide 46: Complex Activation Patterns
variety of activation patterns used in practice e.g. periodic + spontaneous, dual cyclic, on change
timing verification can consider them through use of minimum distance functions
  i.e. specification of the minimum distance between any n consecutive events
  derived from specification or rate-limiter
n
δ(n)
2
3
4
5
6
5ms
10ms
20ms
2 events may come at once
any 5 events are separated by at least 20 ms

## Slide 47: Accounting for BC in Analysis
extend event model propagation for BC
  minimum and maximum value for each router on path
or: test all possible combinations where BC can be consumed on path
  set of possible combinations can be reduced with knowledge on event model propagation
for each possible combination
  check for deadline violation